## Slide 1: ECE 353 Lab 2 Pipeline Simulator

## Slide 2: Aims
Further experience in C programming
  Handling strings
  Further experience in the use of assertions
Reinforce concepts from pipelining
Techniques for simulating parallel operations with a sequential program

## Slide 3: Statement of Work
Write a C program to simulate the register contents of a MIPS machine running an abbreviated instruction set
  Should be cycle-accurate with respect to register contents.
  Simulates a machine consisting of add, sub, addi, mul, lw, sw, beq instructions only.
  Will need to provide some error detection wrt the assembly program input.

## Slide 4: Simulation Approaches
State change in simulation
  Event-driven Simulation: Follows events as they occur.
  Time-driven Simulation: Driven by a clock; does something every clock transition.
Computational Platform
  Sequential: Simpler to program and debug; slower.
  Parallel: More complicated program (need to take interactions into account); much higher throughput (potentially).
Lab 2 involves a sequential, time-driven simulation.

## Slide 5: Inputs to the Simulator
MIPS assembly language program which will be in a file read by the simulator.
Parameters of the simulated machine:
  Memory access time: c cycles.
  Multiply time: m cycles.
  All other EX operations: n cycles.
  ID and WB stages take one cycle to complete their tasks.

## Slide 6: Memory
Separate instruction and data memories (separate address spaces).
Instruction Memory:
  Addressed by the PC.
  Size: 2K bytes (512 words).
Data Memory:
  Accessible to the program.
  Size: 2K bytes (512 words).
Implement both as
linear arrays.

## Slide 7: Processor
Five stages: IF, ID, EX, MEM, WB
Each stage follows the rules you learned in ECE 232, except that IF and EX can take multiple cycles to complete an operation.

## Slide 8: IF
Fetches from the Instruction Memory.
Will have to freeze if there is an unresolved branch.
  Branches are detected in the ID stage.
  When a branch is detected, no further instructions are decoded until the branch is resolved.
  Branches are resolved in the EX stage where a subtraction operation is carried out and the result used to determine if the branch is taken or not.

## Slide 9: ID
Decodes instructions (takes 1 cycle to do this).
Checks for data (RAW) and control hazards.
  Holds up further processing until these hazards have been resolved (no forwarding in this machine).
  Provides the EX stage with the operands it needs.

## Slide 10: EX
Executes the specified operation on the operands it receives from ID.
Can take multiple cycles depending on the operation.
  EX is not itself pipelined; only one instruction can be in EX at any time.
  Use a counter to keep track of ongoing operations.

## Slide 11: MEM
Is only used by the lw and sw instructions.
Receives the data memory address from EX and carries out the data memory read/write operation.
Can take multiple cycles to do this (c cycles).

## Slide 12: WB
Writes back into the register file.
  Will have nothing to do if the instruction does not do a register write.
  Register reads/writes follow the approach in Hennessy & Patterson.

## Slide 13: Simulator Modules
progScanner(): Reads from the file provided by the user, containing the assembly language program. Note that this will have to flexible in dealing with empty spaces.
parser():
  From the instruction passed to it by progscanner(), break it up into its constituent fields (opcode, source registers, immediate field, destination register).
  Detect a certain subset of errors in the program:
    Illegal opcode
    Unrecognized register name
    Register number out of bounds
    Immediate field that is too large

## Slide 14: Simulator Modules (contd.)
Pipeline stage modules:
  IF
  ID
  EX
  MEM
  WB
Pipeline stages will communicate via latches separating them. A latch can only hold information relating to a single instruction.
  Deal with structural hazards.
  Use valid/empty bits to specify if (a) the contents of a latch are valid for use by the stage to its right and (b) the latch is available to be written into by the stage to its left.

## Slide 15: Simulator Execution
We need to simulate parallel operations with a sequential program. How?
  Maintain a counter to represent the clock value.
  Each time the counter increments (representing an advance in time by one cycle), call the stages in reverse order: WB, MEM, EX, ID, IF.
    Why should this work?

## Slide 16: Assertions
Use assertions to help with correctness.
  Assertions should have been thought through and contribute meaningfully to the reliability of the program.
  Preconditions, postconditions, invariants can all be checked. For a good introduction, see http://ptolemy.eecs.berkeley.edu/~johnr/tutorials/assertions.html

## Slide 17: Submission
Summary sheet on Moodle
  Authorship/testing information.
  Call graph of code
  Testing procedures used
  Assertions used
  Results (Seven tables: one for each of the programs provided on the course website).
Upload program code on quark.
  Only a single file should be uploaded: no zipfiles.
ONLY ONE COPY PER GROUP SHOULD BE SUBMITTED.